## Slide 1: Power-efficient memory and caches
Green Computing
Jothini Sritharan

## Slide 2: Introduction

## Slide 3: Motivation
Power-consumption distribution in a SoC Design (Integrated Circuit)

## Slide 4: Content
Revision: Memory organization and caches
Energy consumption concerning memory access
Ideas of reducing power consumption
Low power memory design

## Slide 5: 1. Memory organization and caches
Input:
 address: location of memory which is
accessed
 control: indicates important data;
signals kind of operation
Bidirectional bus:
 data: depending on operation it serves as input or output

## Slide 6
Read operation:
1. row address decoded
 activates word line
2. selection of a row of cells
 transfer of data between cells
and bit lines
3. column decoder chooses bits in right
column and transfers them to data bus

## Slide 7: Cache
„Cache hit“  succesful finding of data
„Cache missing“:
 compulsory miss
 capacity miss
 conflict miss
Cache miss ratio =

## Slide 8: Cache architecture
Cache hit:
tag matches to an element of tag array
Index collects corresponding tag and cache line
Offset chooses right data from selected line

## Slide 9: 2. Energy consumption concerning memory access
The following three main components basically determine the energy consumption:
1. address decoders and word lines
2. data array, sense ampliﬁers and the bit lines
3. the data and address buses leading to the memory

## Slide 10: 3. Ideas of reducing power consumption 3.1 Power-efficient memory Architectures
Partitioning memory and caches
memory array is divided into several
banks  shorter transferring path
because of smaller bit lines

## Slide 11
Additional memory
a small extra cache, which stores recently used
data, is searched first and may prevent
browsing through the whole main cache

## Slide 12
Reducing Tag and Data Array Fetches
Reducing number of accesses by only searching the tags without data first
Then picking only the data of the right tag

## Slide 15: 3.2 Clock-Gating
By connecting the clock with a control signal
by an AND Gatter, the capacitance is only
charged and discharged when control is
on TRUE

## Slide 16: 3.3 Cacheable switching activity
Recurring instructions are stored in a cache
 calculation has to be done only once
Example: For loops
 But only applicable when same input

## Slide 17: 4 Low power memory design
4.1 NOR-Flash-Memory
Fast random access since a transistor can be
individually adressed due to the parallel circuit

## Slide 18
Bit-by-bit-weak program
Applying lower voltage than ordinary
Offset of whole curve
 Lower voltage is needed

## Slide 19: 4.2 Ferroelectric Random Access Memory (FeRAM)
Selecting transistor
Capacitor saves information in form of polarization
Reading: another voltage impulse leads to either a change or a constancy in polarization

## Slide 20
Two stable states at the voltage of 0V
Readout-signal depends on used capacitance
 has a maximum
Jothini Sritharan: Power-efficient memory and caches

## Slide 21: Summary
Memory and caches are responsible for a large share of power-consumption
 necessity for power-efficient caches and memories
General solutions:
Optimization of Cache architecture
Additional memory with most recently used data
Adaption of components like transistors and capacitances